## Slide 1: Using Software Defined Radio to annoy your neighbors
Nikolaos Virvilis

## Slide 2: #whoami
Nikos Virvilis
Cyber Security Background
  Not an RF Engineer
  Using (exploiting) SDR capabilities for Cyber Security / Penetration Testing

## Slide 3: Radio & Software defined Radio
Traditional radio equipment:
  Designed for a specific purpose
  Good luck trying to receive satellite signals with an FM Radio

## Slide 4: Software Defined Radio
RF Receivers or Transceivers
RF (Analog) Input from Antenna  Amplification  Analog to Digital Conversion  Computer
Everything else is performed in software

## Slide 5: What can you do
Listen to FM radio (wow!)
Watch digital TV
  Mess up with your neighbors 
Track airplanes by monitoring their radio transmissions (ADS-B) protocol
  Ships too!
Passive radar (you need 2 SDR dongles and two antennas)
  Btw you can detect “stealth” planes with this
  Listen to Law Enforcement (including TETRA radios), taxi, ham radio etc.

## Slide 6: What can you do (cont.)
  Spoof GPS. Suddenly Google maps tells you that you are in Jamaica
    You can even steal a nice boat 
  Sniff GSM traffic
  Jam Stuff (alarm systems, home automation, etc.)
  Unlock Cars
  And much much more.

## Slide 7: Go cheap
RTL – SDR
  Digital TV receiver
  20 USD
  Use of special drivers allows you to monitor from 24 – 1766 MHz
  R820T2 tuner is considered the best
  E4000 tuner (older chipset): Not so sensitive but can receive 52 – 2200 MHz with a gap from 1100 MHz to 1250 MHz
  Receive Only
  2 MHz bandwidth
  Excellent community support

## Slide 8: A bit more expensive
HackRF One
  Receive AND Transmit
  1 MHz to 6 GHz operating frequency
  20 Mhz bandwidth
  Half – Duplex (i.e. you cannot run OpenBTS )
  300 – 330 euros
  30 mW (15 dBm) max transmit power
  Very good community support

## Slide 9: Even more expensive
BladeRF
  Receive AND Transmit
  300MHz - 3.8GHz operating frequency
  28 Mhz bandwidth
  Full – Duplex (i.e. you can run OpenBTS )
  420 USD (small fpga) – 650 USD (large fpga)
  4mW (6 dBm) max transmit power
  Limited community support

## Slide 10: Pro
USRP B200
  The cheapest of the USRP line
  Receive AND Transmit
  70MHz - 6GHz operating frequency
  56 Mhz bandwidth
  Full – Duplex (i.e. you can run OpenBTS )
  100mW max transmit power
  Decent community support

## Slide 11: (New) kid in the block
LimeSDR / LimeSDR mini
Just released, preliminary reviews are very promising.
It is expected to be comparable to USRP B200 / USRP B210 but at a fraction of the cost
Frequency range: 100 kHz – 3.8 GHz
Bandwidth: 61.44 MHz
Full duplex with 1 or 2 TX/ 1 or 2 RX interface
10mW transmit power

## Slide 12
DEMO

## Slide 13: Radio
GQRX

## Slide 14: ADS-B
  Fine tuned rtl-sdr sticks with integrated Low Noise Amplifier (LNA)
  https://flightaware.com/adsb/prostick/
  Decent antenna
  (Almost) plug and play on a raspberry pi
    https://flightaware.com/adsb/piaware/

## Slide 15: ADS-B – My Node

## Slide 16: ADS-B https://github.com/gvanem/Dump1090

## Slide 17: GSM Traffic

## Slide 18: Hello 

## Slide 19: Capture and Replay
(demo)

## Slide 20: JAM
(demo)

## Slide 21: It’s all about TX power
HackRF: About 15 dBm (31 mW)
  Most Wifi AP’s transmit with 50-100mW
  Even if the transmitter transmits with less that 31 mW, if it is closer to the receiver than the HackRF, you might not be able to jam the signal
  TX Amplifier to the rescue!

## Slide 22: Conclusion
SDR has drastiscally lowered the bar for radio applications
  For both legitimate and nefarious purposes
  Review your Cyber Security posture, considering the low cost attacks that SDR introduces

## Slide 23: Questions
?

## Slide 24: Resources
https://gqrx.dk/
https://github.com/gvanem/Dump1090
https://flightaware.com/adsb/prostick/
https://github.com/sq5bpf/osmo-tetra-sq5bpf
https://github.com/ptrkrysik/gr-gsm
https://www.youtube.com/watch?v=BeeSN14JUYU&list=PLu0BPYzTjiHru1KmPThmbY-8rRm3EWvUQ
https://github.com/merbanan/rtl_433
https://github.com/mossmann/hackrf